## Slide 1
NSDI 2025 · PAPER SUMMARY
MegaStation
Treat a pool of GPUs like one dynamically scheduled processor for massive-MIMO baseband work.
Building Massive MIMO Baseband Processing on a Single-Node Supercomputer
Xincheng Xie · Wentao Hou · Zerui Guo · Ming Liu
5G / vRAN
Massive MIMO
GPU pooling
Dynamic scheduling
Paper and talk materials: USENIX NSDI ’25 [1][2][4]
1 / 13

## Slide 2
THE ONE-SLIDE VERSION
Why this paper exists
Motivation and key insight: [1][2]
2 / 13
PRESSURE
More antennas, more users
Massive MIMO raises radio capacity, but every frame creates substantial baseband computation under millisecond deadlines.
MISMATCH
Static software, irregular GPUs
Frame-, symbol-, and task-level parallelism each work well in some resource states and poorly in others.
OPPORTUNITY
Adapt the pipeline at runtime
MegaStation monitors the GPU pool, changes execution granularity, and schedules urgent ready work.
Thesis: the hardware substrate is not just “more GPUs.” It enables a different software architecture for the RAN.

## Slide 3
WHERE IT FITS
MegaStation lives inside the virtualized baseband unit
Architecture and pipeline: paper §§1–2, Fig. 1 [1]
3 / 13
Phones / devices
Transmit wireless signals
Radio Unit (RU)
Antenna array + digitization
vRAN baseband
MegaStation schedules processing
Mobile core
Routes data and services
UPLINK PIPELINE
FFT → zero forcing → equalization → demodulation → decoding
Radio samples become user data.
DOWNLINK PIPELINE
Encoding → modulation → precoding → IFFT
User data becomes radio samples.
Scope: MegaStation does not redesign the 5G air interface. It redesigns how baseband tasks are executed on compute infrastructure.

## Slide 4
RESEARCH LANDSCAPE
Three hardware directions, three trade-offs
Prior substrates and SNC properties: paper §§1–2 [1]; conference slides [2]
4 / 13
GENERAL-PURPOSE
x86 server clusters
+ Programmable – More servers, physical space, cost, and cross-node coordination at scale BigStation · Hydra
SPECIALIZED
FPGA / fixed accelerators
+ Efficient – Harder to reconfigure, partition, and manage as MIMO settings or traffic change LuMaMi
EMERGING PLATFORM
Single-node supercomputer
+ Dense, programmable GPU pool + Add or remove GPUs while keeping a host-native stack GigaIO FabreX
Open question: If the platform becomes composable, should the baseband software remain statically partitioned?

## Slide 5
THE HIDDEN BOTTLENECK
No single execution granularity wins everywhere
Characterization and “no one-size-fits-all” finding: paper §3 [1]
5 / 13
FRAME LEVEL
large job · low coordination
may waste gaps
SYMBOL LEVEL
symbol
symbol
shuffle
symbol
TASK LEVEL
FFT
equalize
wait
decode
queues / copies
HARDWARE AVAILABILITY CHANGES
Full · fragmented · partial · delayed
The free capacity available to a job changes over time.
THE TRADE-OFF MOVES
Parallelism versus communication
Fine granularity fills gaps; coarse granularity can reduce copying and queueing.

## Slide 6
KEY IDEA
Borrow a processor idea: dynamic instruction scheduling
MegaStation design and processor analogy: paper §4.1 [1]; slides pp. 11–15 [2]
6 / 13
PROCESSOR ANALOGY
→ Baseband task → instruction
→ GPU resources → functional units
→ Data dependencies → instruction graph
→ GPU status → scoreboard
RUNTIME BEHAVIOR
→ Track which work is ready
→ Estimate resources and latency
→ Prioritize by remaining slack
→ Change granularity and placement on the fly
The contribution is a new control plane for computation—not a faster FFT.

## Slide 7
SYSTEM ARCHITECTURE
From incoming frame to the GPU pool
Components and LROC scheduler: paper §§4.1–4.6 [1]
7 / 13
1 · Instruction unit
Parse frames into 11 task types; build dependencies
2 · Scoreboard
Track readiness, execution, resources, and GPU status
3 · Pipeline schedulers
Choose urgent ready work and placement
4 · GPU executors
Run baseband kernels across the pool
DEADLINE POLICY
Least slack first
Urgent frames move ahead.
FILL GAPS
Reorder
Independent ready tasks use idle SMs.
PRESERVE LOCALITY
Coalesce
Related work stays together when useful.
AVOID STALLS
Over-commit
Delayed work enters lower-priority streams.

## Slide 8
A CONCRETE INTUITION
The scheduler changes its answer as resources change
Adaptive granularity and overload behavior: paper §§4.1, 4.4–4.7 [1]
8 / 13
CASE A
One GPU has room
Keep dependent work local and run a coarser unit. Avoid unnecessary transfer. LOCAL
CASE B
Capacity is fragmented
Split into finer ready tasks only when the extra parallelism outweighs shuffling. SPLIT
CASE C
Nothing is free
Use deadlines, queue state, and low-priority execution; shed obsolete frames if overloaded. DELAY
General lesson: Expose application structure—dependencies, deadlines, and locality—to the resource scheduler.

## Slide 9
EVALUATION
Does adaptation pay off?
Evaluation setup and results: paper §§5.1–5.6 [1]. Conference deck displays up to 3× [2].
9 / 13
66.2%
up to lower tail frame-processing latency
4×
up to higher throughput in the paper’s evaluation
1.2–3.6 ms
reported P99.99 latency across tested MIMO configurations
8 RUs
supported under 128×64 MIMO on 6 GPUs in the scale test
What was tested
→ GigaIO FabreX SNC
→ NVIDIA A100 / V100 GPUs
→ Five MIMO configurations
→ Frame-, symbol-, and task-level GPU baselines
→ Scalability, failures, fragmentation, and heterogeneous GPUs
Read carefully: These are maximum results from particular configurations—not a universal 4× speedup.

## Slide 10
CRITICAL READING
Strong result, but not a universal win
Small-MIMO result and methodology: paper §§4.3, 5.1, Appendix A.4 [1]; repository prerequisites [3]
10 / 13
WHAT IS CONVINCING
→ Real implementation on an SNC platform
→ Compares several fixed-granularity strategies
→ Tests fragmentation, scaling, heterogeneity, and GPU availability changes
→ Connects measured behavior to design choices
BOUNDARIES AND CAVEATS
→ For small MIMO, Hydra is faster because MegaStation adds scheduling overhead
→ GPU resource usage is estimated rather than exposed directly
→ The testbed emulates RUs instead of reporting a carrier deployment
→ Reproduction requires NVIDIA Aerial source access
Interpretation: Adaptation helps most when workload size and resource irregularity repay its control overhead.

## Slide 11
BROADER RESEARCH OPPORTUNITIES
The paper opens more questions than “how fast is MegaStation?”
Directions synthesized from design assumptions, evaluation, and related work [1]
11 / 13
1 · RAN-specific GPU interfaces
Predictable preemption, occupancy, and deadline-aware scheduling.
2 · Cross-layer control
Jointly optimize radio scheduling, baseband deadlines, and GPU placement.
3 · Multi-tenant isolation
Give several cells or network functions performance guarantees.
4 · Energy and cost
Reassign or power down accelerators while preserving deadlines.
5 · Heterogeneous accelerators
Span GPUs, FPGAs, DPUs, and future accelerators with one abstraction.
6 · Production validation
Test real fronthaul, mobility, bursts, and long-running carrier operations.

## Slide 12
TAKEAWAY
Three ideas to remember
Synthesis of the paper’s motivation, design, and conclusion [1]
12 / 13
1
The RAN is becoming software infrastructure
Virtualization makes compute scheduling part of wireless-system design.
2
More hardware is not enough
Irregular availability creates a software–hardware parallelism mismatch.
3
Expose structure, then adapt
Dependencies, locality, and deadlines let the runtime rebuild the pipeline.
MegaStation’s bigger contribution is a research pattern: application–platform co-design for composable infrastructure.

## Slide 13
SOURCES
Primary materials
All sources are the course / USENIX materials supplied for this presentation.
13 / 13
[1]
Xie et al. “Building Massive MIMO Baseband Processing on a Single-Node Supercomputer.” NSDI 2025.
https://www.usenix.org/system/files/nsdi25-xie.pdf
[2]
Authors’ NSDI 2025 presentation slides.
https://www.usenix.org/system/files/nsdi25_slides-xie.pdf
[3]
MegaStation source repository, NetLab Wisconsin.
https://github.com/netlab-wisconsin/MegaStation
[4]
Authors’ NSDI 2025 presentation video.
https://www.youtube.com/watch?v=J8n9HY3dcFs
Suggested discussion: Which should adapt first—the radio workload, the software pipeline, or the accelerator scheduler?