## Slide 1
Zhuge
Achieving Consistent Low Latency for Wireless Real-Time Communications with the Shortest Control Loop
Zili Meng et al. · ACM SIGCOMM 2022

## Slide 2
Wireless latency has a long tail
Source: Meng et al., Fig. 2(a)
Fraction of RTT measurements that exceed x
Wireless connections have many more high-RTT events than Ethernet.

## Slide 3
Bandwidth drops fill the AP queue
Source: Meng et al., Fig. 3(a)
10 → 3 Mb/s
7 Mb accumulates each second
until the sender slows down.

## Slide 4
The feedback loop crosses the bottleneck
Source: Meng et al., Fig. 1
Data waits at the AP, crosses wireless, reaches the client,
then feedback returns to the sender.

## Slide 5
Zhuge acts at the access point
Source: Meng et al., Fig. 5
Fortune Teller
Predicts delay when data arrives
Feedback Updater
Signals the sender through feedback

## Slide 6
Fortune Teller estimates wireless delay
Source: Meng et al., Figs. 6–7
totalDelay = qLong + qShort + tx
qLong
queue size ÷ average departure rate
qShort
front packet waiting time
tx
wireless transmission interval
qShort reacts first after the bandwidth drop.

## Slide 7
Feedback Updater uses earlier ACKs
Source: Meng et al., Fig. 9

## Slide 8
Trace simulations show fewer delays
Source: Meng et al., Figs. 11 and 13
45–75%
fewer RTT events above 200 ms
38–92%
fewer video frames delayed
more than 400 ms
RTP/RTCP across five wireless traces, compared with the best baseline

## Slide 9
OpenWrt testbed improves latency
Source: Meng et al., Fig. 18
17–95% fewer high RTT events
9–67% fewer delayed frames

## Slide 10
Scope and limitations
Source: Meng et al., §6–7 and Fig. 19
Last-mile downlink
Applying it to the wireless first mile
would require client integration.
Prediction error
Estimates become less accurate at high delays.
Severe bandwidth drops
Loss and TCP timeouts can limit the benefit.

## Slide 11
Takeaway
Meng et al., SIGCOMM 2022
Use feedback already returning to the sender
Sender adapts sooner, the queue stays shorter
Predict delay at AP