## Slide 1: From Efficient Motion Recognition to Geometry-Aligned Motion Reasoning
Jackie Ye

## Slide 2: Today's Outline
Introduction to Human Action Recognition (HAR)
Principles of Wi-Fi Sensing for Human Mesh Construction
3D mesh-based human action recognition on edge devices
  ARiSE: Efficient Mesh-Based HAR at the Edge
Empower Large Language Models (LLMs) to deeply understand human motion.
  GeoMotionGPT: Geometry-Aligned Motion Understanding

## Slide 3: Sensing Modalities in HAR
Vision-Based (RGB/Depth)
RF-Based (Radar/LiDAR)

## Slide 4: The Vision Dilemma
Privacy Risks: Cameras capture highly identifiable visual data
Line-of-Sight Dependency: Highly vulnerable to physical occlusions, blind spots, and low-light conditions
Deployment Friction: Unsuitable for sensitive spaces
  e.g., bedrooms, healthcare

## Slide 5: The Mechanics of Wi-Fi Sensing
Channel State Information (CSI)
  Captures minute signal reflections from the human body and the environment.
  Extracts multi-dimensional spatial dynamics.
Angle of Arrival (AoA)
  Can be extracted from CSI
  Isolates target movements from static multi-path clutter.
Y. Wang et al., "Wi-Mesh", ACM SenSys 2022.

## Slide 6: Wi-Fi-based Human Mesh Estimation
Y. Wang et al., "Wi-Mesh", ACM SenSys 2022.

## Slide 7: Skinned Multi-Person Linear (SMPL) Model
A standardized, high-fidelity mesh comprising 6,890 vertices.
Decomposes complex human bodies into low-dimensional Shape and Pose parameters.
Uses linear blend skinning to accurately model joint deformations and soft-tissue dynamics.

## Slide 8: Performing HAR on SMPL model
Mesh VS. Skeleton: Mesh sequences capture rich surface dynamics and fine-grained articulated movements (e.g., fingers and torso rotation) missed by simple skeletons.
The Bottleneck: Processing sequences of 6,890 vertices per frame creates a massive computational burden, overwhelming edge devices.
  >287x increase in spatial computational overhead for a standard CNN.
The Challenge: Overwhelming for resource-constrained edge devices.
  Thus, applying down-sampling algorithm is necessary

## Slide 9: Furthest Point Sampling (FPS) Algorithm
Core Mechanism: Iteratively selects the point that is farthest away from the sampled set.
The Advantage: Provides a uniform, well-distributed geometric coverage.
However: it treats all body parts equally. Over-samples static regions (abdomen), loses critical details (hands/fingers)
Original
Output(N=256)

## Slide 10: Why Sampling Matters
The Flaw: Global FPS wastes points on static areas (Abdomen: 53 vertices, 0.1% impact).
The Cost: Starves critical motion joints (Arms: 8 vertices, 20.05% drop!).
Our Solution: Partitions the mesh to force high point density on high-value regions (hands/limbs).

## Slide 11: Overall Architecture of ARiSE

## Slide 12: Results of ARiSE

## Slide 13: Ablation Studies

## Slide 14: Empowering HAR Using LLM
The Paradigm Shift: LLMs unlock complex, unified motion-language reasoning.
The Bridge (Tokenization): Quantizing continuous 3D motions into discrete "motion words" (Codebook IDs).

## Slide 15: Vector Quantized Variational Auto Encoder (VQ-VAE)

## Slide 16: VQ-VAE-based Motion Understanding
B. Jiang et al., "MotionGPT: Human motion as a foreign language", NeurIPS 2023.

## Slide 17: Problems of VQ-VAE-based Approaches
Geometric Disconnect: Decouples quantization from semantic learning. Linking modalities solely via Token IDs destroys the intrinsic 3D geometric structure.
Optimization Block: The non-differentiable nearest-neighbor assignment blocks geometry-aware gradients, preventing fine-grained structural control.
Codebook Collapse: Exhibits a severe heavy-tailed usage pattern. A few tokens dominate while many become "dead codes," resulting in overly collapsed and repetitive motion dynamics.

## Slide 18: Overall Architecture of GeoMotionGPT

## Slide 19: Experiment Results of GeoMotionGPT

## Slide 20: Experiment Results (Con't)

## Slide 21: Ablation Studies