## Slide 1
SAGE
Predicting the next milliseconds of 5G
How predictive radio scheduling changes the uplink resource tradeoff
A high-level architecture and research-landscape presentation
CIS 4930/5930 Future Edge Network
Victor Liu
Notes: 5G is often introduced as a faster way to use a phone. But its larger promise is more important: it could support applications that need communication to be fast, reliable, and predictable.
For example, imagine a surgeon controlling a robotic system from another location. The surgeon sends movement commands to the robot, while video and sensor feedback travel back. Even a small and unpredictable delay could make the system difficult to control.
5G alone does not make remote surgery safe. Specialized equipment, redundancy, and many other systems are also required. But this example shows why low and predictable latency matters.
To support applications like this, the network must reduce more than the time required to transmit data. It must also reduce the time devices spend waiting for permission to transmit.
That is the specific problem Sage studies.

## Slide 2
5G has two different paths
User data moves through the network; control decisions determine when it may move
WHO CARRIES?
UE
5G base station
gNB
5G Core
AMF · SMF · UPF
Application
server
uplink data
MAC scheduler
WHO DECIDES?
Sage sits beside this decision point. It changes when and how the base station allocates shared radio resources.
The paper improves a decision loop inside the Radio Access Network (RAN), not the packet-forwarding path.
02
Paper §§1–2, 4; study guide
Notes: To understand the problem, we need to separate two parts of the network.
The first is the data path. A device sends information through the 5G base station and then toward an application server.
The second is the decision path. The base station must decide when the device is allowed to use the shared radio resources.
This distinction is important. Sage does not make the application data travel through a new network location. Instead, it improves the decision that controls access to the radio.
In simple terms, the network already knows how to carry the data. Sage tries to help it decide earlier when the data is coming.

## Slide 3
1G to 5G: more flexible networks, harder coordination
The paper belongs to the latest step in a longer shift from reserved voice paths to programmable shared infrastructure
1G
Analog voice
Reserve a circuit
2G
Digital voice
Add packet data
3G
Richer data
More varied traffic
4G
Packet core
Schedule shared radio
5G
Modular + flexible
Software can improve decisions
THE RECURRING SYSTEMS PROBLEM
Every era must decide who gets access to scarce network resources, and when.
Sage keeps the 5G architecture, then improves the information available to the scheduler.
reserved path
shared radio
more demand, more scheduling
03
Study guide: historical connection; paper §1
Notes: In early cellular networks, the main goal was to connect voice calls. The network could reserve a communication path for one conversation.
As cellular systems developed, they began supporting internet data, video, sensors, games, industrial machines, and other applications. These applications do not all send data continuously. Many of them produce short bursts at unpredictable times.
That means the network must share the same radio resources among many different users and applications.
5G gives the network more flexibility and software control, but that flexibility creates more decisions. The system must decide which device should transmit, when it should transmit, and how much capacity it should receive.
Sage focuses on improving one of those decisions.

## Slide 4
The 5G link has two directions
Sage focuses on the device-to-network direction, where the base station must wait to learn what the device will send
User equipment
(UE)
gNB
shared radio
Network + app
server / service
UPLINK
camera frame · sensor burst · game command
DOWNLINK
video frame · map update · control response
Sage: predictive uplink
scheduling
Downlink remains an important scope question: the network knows more about queued data, but shared radio capacity and channel conditions still need scheduling.
04
Paper §§1–2, 10; study guide
Notes: There are two directions of communication.
The uplink is when the device sends information to the network. For example, a surgical robot might send sensor data, a camera might send a video frame, or a phone might send a game command.
The downlink is when the network sends information back to the device. This could include a video frame, a control response, or an updated map.
Sage focuses on the uplink because the device knows when its application creates data, while the base station controls the radio resources. The base station has to learn about the device’s demand through signaling.
That difference between who creates the data and who controls the radio is the central information gap in the paper.

## Slide 5
Fast radio can still spend time waiting
A grant-based uplink learns about a burst through a signaling sequence
1
SR
Scheduling Request
2
Grant
permission to transmit
3
Data + BSR
payload plus queue estimate
4
More grant
resources for backlog
WAITING LIVES BETWEEN THE BOXES
SR timing can be a large part of the startup delay
The paper reports that a Scheduling Request can take up to 40 ms in the relevant configuration. The exact delay depends on configuration and traffic state.
Capacity exists
but the device waits
05
Paper §§1–3, Fig. 1; author slides 6–9
Notes: Let us follow one burst of data from the device.
Suppose a robot’s camera creates a large image, but the robot does not currently have enough resources to transmit it.
First, the device sends a Scheduling Request, or SR. It is saying, “I have data waiting.”
The base station then sends a grant. The grant is permission to use specific radio resources.
The device sends some of the data and also sends a Buffer Status Report, or BSR. The BSR tells the base station approximately how much data is still waiting.
If the burst is large, the base station may need to send another grant before the rest of the data can be transmitted.
So the device and the base station communicate back and forth before the full burst is delivered. Each step may be short, but the waiting adds up.
This is why a fast radio connection can still produce noticeable application latency.
Optional: The paper reports that the Scheduling Request can take up to 40 milliseconds in the relevant configuration. That number is configuration-dependent, not a universal delay for every 5G connection.

## Slide 6
The scheduler faces a latency–waste tradeoff
Two familiar policies sit at opposite ends; Sage tries to use prediction between them
Request-based
grant-based
Ask when data is ready
low idle allocation
waiting adds latency
Preallocated
grant-free baseline
Reserve capacity ahead
fast access
unused capacity
Predictive
Sage
Forecast time + size
targeted reservation
prediction errors
Sage’s goal is a better operating point, not a free lunch: lower waiting with a controlled resource premium.
06
Paper §1, §7A; study guide
Notes: The network has two obvious choices.
With request-based, or grant-based, scheduling, the network waits until a device asks for resources. This avoids reserving capacity unnecessarily, but the request and response create waiting time.
With preallocated, or grant-free, access, the network reserves capacity before the device asks. This can reduce waiting, but the reserved capacity may be empty or too small.
Sage tries to find a better balance. It predicts when the next burst will arrive and approximately how large it will be. The base station can then prepare a more targeted allocation.
The benefit is less waiting. The cost is that the network may reserve some extra resources because predictions are never perfect.
This is the point where Sage enters the story: it uses prediction to improve the existing scheduling tradeoff.

## Slide 7
Sage first makes the traffic interpretable
The base station sees delayed fragments; the application thinks in bursts
HIDDEN APPLICATION BURST
one video frame / sensor burst
WHAT THE GNB OBSERVES
fragments arrive at different times
TRAFFIC TRAIN ABSTRACTION
group nearby observations into one predicted burst
next burst
time + size
A better representation gives the model something meaningful to predict.
07
Paper §3, Figs. 2–5; author slides 15–33
Notes: The base station does not directly see the exact moment when the application created its data.
For example, one video frame may be divided into several pieces. Those pieces may arrive at different times because of scheduling, retransmissions, or changing radio conditions.
If the system treats every piece as a separate new event, it may misunderstand the application.
Sage groups nearby arrivals into what it calls a traffic train. You can think of this like a warehouse receiving several boxes from one shipment. The warehouse should recognize that the boxes belong to one order instead of treating them as unrelated orders.
Once Sage creates this cleaner representation, it can predict the next burst’s arrival time and size.

## Slide 8
Sage is a complete control loop
Prediction matters only when it reaches the scheduler in time and knows when to back off
Sage
predict → allocate → learn
Traffic
characterization
Model selection
and verification
Error monitoring
and fallback
Continual learning
and database
real-time RIC near gNB
fast loop
near-real-time loop
Immediate decisions stay local. Heavier model selection and updates can use a slower control loop.
08
Paper §§4–6, Fig. 6; author slides 39–44
Notes: Sage is more than a machine-learning model.
First, it observes and characterizes the traffic. Then it selects and checks a model that seems appropriate. The fast part of the system predicts the next burst and helps schedule resources.
After that, Sage monitors its own mistakes. It can learn from new traffic, update its model database, and fall back to ordinary scheduling when its predictions are not reliable.
This is why the system uses different control timescales. Fast decisions need to happen close to the base station. Heavier tasks, such as model selection and larger updates, can happen more slowly.
A prediction is only useful if it arrives before the transmission opportunity.

## Slide 9
A useful analogy: radio resources behave like data-center power
Better forecasts can reduce both waiting and waste, but the analogy is conceptual rather than a measured energy result
NETWORK SCHEDULING
DATA-CENTER OPERATIONS
Demand arrives in bursts
Jobs spike with user traffic
Reserve resource blocks
Reserve servers / power / cooling
Too little allocation
Queueing and missed deadlines
Too much allocation
Idle capacity and wasted energy
Predict time + size
Forecast load before the spike
The research question scales beyond 5G: how early must a system predict demand to allocate only what it needs?
09
Conceptual analogy proposed for this presentation; Sage paper §§1, 7
Notes: A useful analogy is data-center power management.
Imagine a data center that receives large jobs throughout the day. If it waits until a job arrives before starting servers, the job may sit in a queue.
But if it keeps every server, cooling system, and power supply ready all the time, it wastes energy.
Radio scheduling has a similar tradeoff. Too little resource allocation causes waiting. Too much allocation wastes capacity.
If the system can predict when a workload will arrive and how large it will be, it can prepare more accurately.
This analogy helps show why prediction matters beyond cellular networks.

## Slide 10
The result is a better tradeoff, with a measurable cost
Keep each headline attached to its comparison baseline
NORMALIZED TO 1.0× GRANT-BASED ACCESS
Chart: 
| Uplink latency | Allocated resources
Relative to grant-based | 0.4 | 1.59
2.53×
lower average uplink latency vs grant-based
1.59×
allocated resources vs grant-based
up to 37.5× fewer resources
vs evaluated grant-free baselines
12
Paper abstract, §§1, 7A; author slide 50
Notes: This chart compares Sage with grant-based scheduling, using the grant-based result as 1.0.
The paper reports a 2.53-times reduction in average uplink latency. In simpler terms, the new latency is approximately 40 percent of the original latency.
The cost is that Sage uses about 1.59 times as many allocated resources in this comparison. That extra allocation helps the system prepare for uncertainty in its predictions.
The third number must be interpreted separately. Sage uses up to 37.5 times fewer resources than the evaluated grant-free baselines.
That does not mean Sage is 37.5 times better than grant-based scheduling. The comparison baseline is different.

## Slide 11
Radio latency is only one stage of application latency
Sage improves the network path; decoding, processing, and display remain
radio
uplink delivery
compute
decode / process
experience
display / response
2.07–2.54×
video network latency
1.13–1.23×
end-to-end display latency
A network improvement does not translate one-for-one into a user-visible improvement.
13
Paper §§1, 7C; author slide 52
Notes: Even if the radio delivers data faster, the user may not see the result immediately.
For example, a video frame still has to be decoded, processed, and displayed.
The paper reports that video network latency improved by approximately 2.07 to 2.54 times. But the end-to-end display latency improved by only about 1.13 to 1.23 times.
This is an important systems lesson. Improving one stage of a pipeline does not automatically improve the entire application by the same amount.
The network can become faster while computation and display still limit the final experience.

## Slide 12
Where Sage fits in the research landscape
A useful comparison asks where each system observes demand, predicts, and acts
Research thread | Where it observes | What it changes | Connection to Sage
Device-side anticipation | At the device | Advance messages prepare the network | Sage moves prediction to the base station
Programmable RAN control | Near radio processing | Places decisions close to deadlines | Sage applies this to scheduling
Sage | gNB traffic observations | Predicts next burst time + size | Proactive allocation with fallback
Common theme: use information earlier, then place the decision close enough to act.
15
Paper §9; EdgeRIC NSDI 2024; device-based LTE latency NSDI 2021
Notes: This table compares different research directions by asking where they observe demand and where they make decisions.
Some systems use advance messages from the device to prepare the network. Other research studies how to place intelligent control close to the radio so decisions can happen quickly.
Sage combines these ideas with a specific prediction problem. It observes traffic near the base station and predicts the next uplink burst.
The important question is not simply, “Which model is more advanced?”
The better question is: what does the system observe, what does it predict, where does the decision happen, and can the system act before the deadline?
Optional: Avoid directly comparing speedup numbers across papers because their testbeds and baselines are different.

## Slide 13
What about the downlink?
The uplink information gap is different from the downlink information gap
UPLINK
Device → network
app creates
data
gNB learns
through SR / BSR
Sage predicts before the request sequence completes.
DOWNLINK
network → device
server / gNB
knows queued data
shared radio
+ channel
The network has better visibility, but capacity and channel quality still shape the schedule.
Open question: can predictive control coordinate both directions with edge computation and mobility?
14
Paper scope and future-work framing; §§1, 7, 10
Notes: Sage focuses on the uplink because the device knows when its application creates data, while the base station has to discover that demand through signaling.
The downlink has a different information situation. The network usually knows more about the data waiting to be sent.
However, downlink scheduling still has challenges. The radio is shared, channel quality changes, users may move, and different applications may have different deadlines.
So downlink is a natural direction for future research. We should describe it as a scope question, not as an additional Sage result.

## Slide 14
The paper opens a wider research agenda
Sage’s architecture exposes where future network intelligence still has to improve
01
Better observation
Detect traffic trains when SR periods are long and observations arrive late
02
Traffic + channel prediction
Predict demand and radio quality together
03
Cross-slice coordination
Resolve competing predictions over shared physical resources
QUESTIONS FOR THE NEXT PAPER
How should uncertainty determine reservation size?
Can models transfer across cells, users, or applications?
How should radio, edge compute, energy, and fairness be optimized together?
16
Paper §10; study guide
Notes: The authors identify three main directions.
First, Sage needs better traffic-train detection when scheduling requests arrive less often and the observations are delayed.
Second, the system could predict both traffic demand and channel quality. Knowing that a large burst is coming is useful, but the network also needs to know how difficult that burst will be to transmit.
Third, predictive scheduling could be coordinated across network slices. Different services may share the same physical radio even if they are logically separated.
The broader questions are also interesting. How much extra capacity should we reserve when the prediction is uncertain? Can models transfer to new cells or applications? Can radio scheduling and edge computing be planned together?

## Slide 15
The central lesson
Sage treats 5G as a platform that can be redesigned at the decision points
Observe
Recover a useful view of demand
Predict
Estimate the next burst before it arrives
Allocate
Prepare only the resources the schedule can justify
The broad research opportunity is simple to state:
How can a network make a good decision early enough to matter?
Sage answers one version of that question for the 5G uplink.
17
Synthesis of paper §§1–10
Notes: The central loop is simple: observe, predict, and allocate.
First, the network needs a useful representation of the traffic. Second, it predicts the next burst before it arrives. Third, it prepares radio resources close to the time they are needed.
The broader lesson is that 5G is not just a collection of components to memorize. It is a platform with decision points that researchers can redesign.
Sage improves one of those decision points by making the scheduler more proactive.
The larger question is: how can a network make a good decision early enough to matter?
Sage provides one answer for the 5G uplink: predict the demand, allocate ahead of time, monitor the errors, and fall back when the prediction is not trustworthy.