## Slide 1
01
FUTURE EDGE NETWORKS
A Brief History
of Wi‑Fi
Protocols, PHY waveforms, and the design choices behind 802.11b → be — plus the 60 GHz ad/ay branch
frequency
CIS4930 / CIS5930
Notes: • Open with a familiar question: why does the Wi‑Fi icon look unchanged while the radio underneath has changed repeatedly?
• The lecture follows two threads: historical standardization and the PHY resource dimensions used to gain capacity.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://extr-p-001.sitecorecontenthub.cloud/api/public/content/3f5d887b048d49cba95392b829960d1b?download=true&v=564c5124

## Slide 2
WI-FI HISTORY
Wi‑Fi improved by spending new resource dimensions
02
SPECTRUM
2.4 → 5 → 6 → 60 GHz
BANDWIDTH
20 → 40 → 80 → 160 → 320 MHz
CONSTELLATION
BPSK → 64/256/1024/4096‑QAM
SPACE
SISO → SU‑MIMO → MU‑MIMO
SCHEDULING
one user → OFDMA resource units
LINKS
one band → multi‑link operation
Notes: • Use this as the organizing framework for the whole lecture.
• Every later amendment keeps the core 802.11 family identity but adds one or more dimensions for peak rate, capacity, reliability, or latency.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://standards.ieee.org/ieee/802.11be/7516/
- https://www.cisco.com/c/en/us/products/collateral/wireless/white-paper-c11-740788.html

## Slide 3
WI-FI HISTORY
An amendment name and a Wi‑Fi generation are not the same thing
03
IEEE amendment
Market name
PHY shorthand
802.11b
Wi‑Fi 1
HR‑DSSS / CCK
802.11a
Wi‑Fi 2
OFDM at 5 GHz
802.11g
Wi‑Fi 3
OFDM at 2.4 GHz
802.11n
Wi‑Fi 4
HT: MIMO + 40 MHz
802.11ac
Wi‑Fi 5
VHT: wider + 256‑QAM
802.11ax
Wi‑Fi 6 / 6E
HE: OFDMA + 1024‑QAM
802.11be
Wi‑Fi 7
EHT: MLO + 320 MHz
802.11ad / ay
WiGig
Directional 60 GHz
Notes: • Explain that IEEE names technical amendments; the Wi‑Fi Alliance later introduced simpler generation names.
• 802.11ad and 802.11ay are a parallel 60 GHz branch commonly associated with WiGig rather than the numbered Wi‑Fi 1–7 sequence.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/
- https://helpfiles.keysight.com/csg/n7637/Content/Main/802.11ad%20Concepts.htm

## Slide 4
WI-FI HISTORY
Four milestones made consumer Wi‑Fi possible by 1999
04
1971
ALOHAnet
Wireless packet networking proves shared radio access.
1985
Unlicensed ISM
FCC opens spectrum for spread-spectrum systems.
1990–97
IEEE 802.11
A common MAC/PHY standard replaces vendor islands.
1999
Wi‑Fi
802.11a/b and interoperability certification arrive.
Notes: • Connect ALOHAnet to random access, then connect unlicensed spectrum to permissionless innovation.
• The 1997 base standard existed before the Wi‑Fi brand; 1999 is the commercial inflection point with 802.11a/b and interoperability certification.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://extr-p-001.sitecorecontenthub.cloud/api/public/content/3f5d887b048d49cba95392b829960d1b?download=true&v=564c5124

## Slide 5
WI-FI HISTORY
The recognizable 802.11 protocol lives above changing PHYs
05
LLC / IP / applications
Outside 802.11
802.11 MAC
Association • framing • ACK • security • CSMA/CA
PLCP
Preamble • header • rate signaling • PPDU format
PMD / waveform
DSSS • OFDM • MIMO • OFDMA • single carrier
Same family
Different ways to turn bits into radio energy
PHY evolution
Notes: • Define a PPDU as the PHY-layer transmission unit placed on air.
• The MAC delivers familiar behaviors across generations, while PLCP/PMD details define the preamble, coding, modulation, channel width, and spatial streams.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 6
WI-FI HISTORY
The 1997 baseline solved shared access before it solved speed
06
COMMON MAC IDEA
Listen → wait → random backoff → transmit → ACK
sense
→
DIFS
→
backoff
→
DATA
→
ACK
Original PHY choices
2.4 GHz
1 or 2 Mb/s
FHSS
DSSS
Infrared option
CSMA/CA avoids collisions; it cannot detect them while transmitting.
Notes: • Contrast Ethernet collision detection with wireless collision avoidance.
• A station may not hear every other station, and its own transmission overwhelms the receiver; hence carrier sense, random backoff, positive ACK, and optional RTS/CTS.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 7
WI-FI HISTORY
802.11b made 2.4 GHz practical with coded spreading
07
11 Mb/s
maximum PHY rate
≈22 MHz
channel width
2.4 GHz
band
One symbol becomes a patterned chip sequence
+
+
−
+
−
−
+
−
CCK encodes information in the phase relationships of code words; spreading provides processing gain and robustness.
PHY path
bits
→
CCK code
→
DSSS
1 / 2 Mb/s: Barker coding
5.5 / 11 Mb/s: CCK
Notes: • Start with 802.11b because DSSS is intuitive: replace each symbol with a longer chip pattern.
• Avoid saying that CCK merely repeats bits. It selects complex code words whose phases carry multiple bits while preserving useful correlation properties.
• The familiar three non-overlapping 2.4 GHz channels in North America arise because the occupied channels are much wider than their 5 MHz center spacing.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 8
WI-FI HISTORY
802.11a replaced spreading with many orthogonal subcarriers
08
54 Mb/s
maximum rate
20 MHz
channel
5 GHz
band
OFDM spectrum: overlapping subcarriers, orthogonal at sampling points
frequency →
20 MHz OFDM
64-point FFT
48 data subcarriers
4 pilot subcarriers
BPSK to 64-QAM
6–54 Mb/s
Notes: • Explain orthogonality operationally: each subcarrier is sampled where the others cross zero, allowing spectra to overlap without ideal inter-carrier interference.
• The cyclic prefix converts multipath delay spread into a manageable guard interval and supports simple frequency-domain equalization.
• 802.11a reached 54 Mb/s but early 5 GHz propagation and device cost slowed mass adoption relative to 802.11b.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 9
WI-FI HISTORY
802.11g brought the 802.11a waveform back to 2.4 GHz
09
802.11b neighborhood
2.4 GHz
DSSS / CCK
802.11a engine
OFDM
up to 54 Mb/s
+
Backward-compatible mixed networks pay protection overhead when legacy 802.11b stations are present.
Notes: • Frame 802.11g as a strategic recombination: the OFDM PHY ideas of 802.11a in the popular 2.4 GHz ecosystem.
• Backward compatibility accelerated adoption but created mixed-mode protection overhead.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 10
WI-FI HISTORY
802.11n scales rate in bandwidth, space, and time
10
40 MHz
channel bonding
4 streams
SU‑MIMO
64‑QAM
denser symbols
A‑MPDU
frame aggregation
Antenna arrays turn multipath from an impairment into parallel spatial streams.
AP
STA
2.4 + 5 GHz
Notes: • 802.11n is the major architectural jump: MIMO, channel bonding, short guard interval, and aggregation work together.
• Maximum standardized configuration reaches 600 Mb/s using four spatial streams, 40 MHz, 64-QAM 5/6, and short GI; typical client devices implement fewer streams.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://www.cisco.com/c/en/us/support/docs/wireless-mobility/wireless-lan-wlan/212892-802-11ac-wireless-throughput-testing-and.html

## Slide 11
WI-FI HISTORY
802.11ac pushes the 5 GHz OFDM formula harder
11
160 MHz
up to 80+80 / 160
256‑QAM
8 bits per symbol
8 streams
standard maximum
DL MU‑MIMO
Wave 2 capability
Wider
20
+ 40 + 80 + 160 MHz
Tighter
More users
AP
U1
U2
U3
Notes: • Summarize 802.11ac with Cisco's memorable dimensions: wider channels, tighter modulation, more spatial streams, and downlink MU-MIMO.
• 256-QAM carries 8 coded bits per subcarrier symbol but requires higher SNR than 64-QAM.
• Maximum PHY rates are configuration ceilings, not expected application throughput.
[Sources]
- https://www.cisco.com/c/en/us/td/docs/wireless/controller/technotes/8-4/b_cisco_aironet_series_migrating_to802_11_ac.html
- https://www.cisco.com/c/en/us/support/docs/wireless-mobility/wireless-lan-wlan/212892-802-11ac-wireless-throughput-testing-and.html

## Slide 12
WI-FI HISTORY
802.11ax optimizes dense efficiency, not only peak speed
12
Before: one user occupies the channel
802.11ax: users share frequency in one PPDU
one scheduled user
four resource-unit allocations
OFDMA
frequency scheduling
UL + DL MU‑MIMO
spatial scheduling
1024‑QAM
10 bits/symbol
BSS coloring
spatial reuse
TWT
power scheduling
Notes: • OFDMA is the conceptual center: an AP partitions OFDM subcarriers into resource units for multiple stations in the same transmission opportunity.
• 802.11ax adds frequency as a multiuser allocation dimension on top of time and space.
• The design target is high efficiency in dense deployments, not simply a larger single-link headline rate.
[Sources]
- https://www.cisco.com/c/en/us/products/collateral/wireless/white-paper-c11-740788.html
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 13
WI-FI HISTORY
802.11ax uses 4× narrower subcarrier spacing
13
802.11a/g/n/ac
312.5 kHz spacing • 3.2 μs useful symbol
802.11ax HE
78.125 kHz spacing • 12.8 μs useful symbol
4× more FFT points in the same 20 MHz channel
Longer symbols improve tolerance to delay spread and create finer-grained resource units; guard intervals adapt to the environment.
Notes: • For a 20 MHz channel, legacy OFDM uses 312.5 kHz subcarrier spacing and 3.2 μs useful symbol time; HE OFDM uses 78.125 kHz and 12.8 μs.
• A longer OFDM symbol reduces the relative cost of a longer guard interval and creates more subcarriers that can be grouped into resource units.
• The diagram is conceptual and not a literal spectrum mask.
[Sources]
- https://www.cisco.com/c/en/us/products/collateral/wireless/white-paper-c11-740788.html

## Slide 14
WI-FI HISTORY
Wi‑Fi 6E adds spectrum, not a new 802.11 waveform
14
2.4 GHz
range + legacy
5 GHz
capacity + mature ecosystem
6 GHz
clean wide channels for Wi‑Fi 6E/7
Same HE PHY/MAC toolbox
New operating spectrum and channel plan
A band extension is not the same as a new IEEE amendment.
Notes: • Clarify the naming trap: Wi‑Fi 6E is Wi‑Fi 6 / 802.11ax extended into 6 GHz; it is not a separate PHY generation.
• Regulatory channel availability varies by country, so avoid implying identical 6 GHz allocations worldwide.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://www.cisco.com/c/en/us/support/docs/wireless-mobility/wireless-lan-wlan/212892-802-11ac-wireless-throughput-testing-and.html

## Slide 15
WI-FI HISTORY
802.11be makes several links behave like one connection
15
AP
STA
2.4 GHz
5 GHz
6 GHz
MULTI‑LINK OPERATION
320 MHz
channel width
4096‑QAM
12 bits/symbol
puncturing
use clean subchannels
>30 Gb/s
required max mode
Notes: • MLO lets a device establish and coordinate links across bands; implementations can use links for throughput, load balancing, redundancy, or latency reduction.
• 802.11be adds 320 MHz channels, 4096-QAM, flexible puncturing, and other enhancements while preserving backward compatibility.
• IEEE 802.11be-2024 requires at least one mode supporting at least 30 Gb/s at the MAC service access point; marketing peak PHY figures may be higher.
[Sources]
- https://standards.ieee.org/ieee/802.11be/7516/
- https://standards.ieee.org/ieee/802.11/10548/

## Slide 16
WI-FI HISTORY
802.11ad uses enormous bandwidth at 60 GHz
16
2.16 GHz
channel width
≈6.8 Gb/s
maximum PHY rate
room scale
range
Three PHY modes
Control PHY: robust spread BPSK
Single‑carrier PHY: practical high rate
OFDM PHY: multicarrier option
AP
STA
Beam training is essential
Notes: • 802.11ad is the Directional Multi-Gigabit branch around 60 GHz.
• Its 2.16 GHz-wide channels make multi-gigabit rates possible without relying only on extremely dense modulation.
• High path and penetration loss shrink coverage but enable directional reuse; beam training aligns transmit and receive sectors.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://helpfiles.keysight.com/csg/n7637/Content/Main/802.11ad%20Concepts.htm
- https://www.keysight.com/us/en/assets/7018-03292/application-notes/5990-9697.pdf

## Slide 17
WI-FI HISTORY
802.11ay turns the 60 GHz link into a wider, spatial system
17
802.11ad
one 2.16 GHz channel
directional single link
802.11ay
channel bonding + MIMO
at least one ≥20 Gb/s mode
→
60 GHz evolves from a cable-replacement idea toward high-capacity access and backhaul.
Notes: • 802.11ay enhances operation in license-exempt bands above 45 GHz and requires at least one mode delivering at least 20 Gb/s at the MAC service access point.
• Key extensions include channel bonding/aggregation, MIMO, improved beamforming, and longer-range use cases.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://standards.ieee.org/wp-content/uploads/import/documents/other/geps_07-iot_smart_cities.pdf

## Slide 18
WI-FI HISTORY
Four waveform ideas explain most of Wi‑Fi’s PHY history
18
DSSS / CCK
Spread symbols across chips
OFDM
Parallel orthogonal tones
OFDMA
Assign tone groups to users
60 GHz SC
Very wide directional carrier
Waveform choice follows the channel: interference, delay spread, bandwidth, mobility, and hardware constraints.
Notes: • Use this slide for retrieval practice: ask students to match standards to waveform families.
• DSSS/CCK: 802.11b. OFDM: 802.11a/g/n/ac and the basis of ax/be. OFDMA: multiuser extension emphasized by ax/be. 60 GHz single carrier: widely used in ad and enhanced by ay.
• The sketches are conceptual, not calibrated time-domain or spectrum-mask plots.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://www.cisco.com/c/en/us/products/collateral/wireless/white-paper-c11-740788.html
- https://helpfiles.keysight.com/csg/n7637/Content/Main/802.11ad%20Concepts.htm

## Slide 19
WI-FI HISTORY
The mainstream branch evolves continuously from b to be
19
802.11
year
GHz
MHz
key PHY idea
headline maximum
b
1999
2.4
≈22
CCK
11 Mb/s
a
1999
5
20
OFDM
54 Mb/s
g
2003
2.4
20
OFDM
54 Mb/s
n
2009
2.4/5
20/40
OFDM + MIMO
600 Mb/s
ac
2013
5
20–160
OFDM + MU‑MIMO
6.9 Gb/s
ax
2021
2.4/5/6*
20–160
OFDMA + MU‑MIMO
9.6 Gb/s
be
2024
2.4/5/6
20–320
EHT + MLO
≥30 Gb/s†
* 6 GHz via Wi‑Fi 6E certification / regulation. † IEEE 802.11be requirement is measured at the MAC SAP.
Notes: • Treat the maxima as comparison anchors, not promised throughput.
• The years are standard milestones; commercial availability and Wi‑Fi certification dates can differ.
• The standards allow configurations beyond what typical phones and access points implement.
[Sources]
- https://standards.ieee.org/wp-content/uploads/interactive/web/wi-fi-timeline/index.html
- https://standards.ieee.org/ieee/802.11/10548/
- https://standards.ieee.org/ieee/802.11be/7516/
- https://www.cisco.com/c/en/us/support/docs/wireless-mobility/wireless-lan-wlan/212892-802-11ac-wireless-throughput-testing-and.html

## Slide 20
WI-FI HISTORY
A PHY rate is the product of several optimistic choices
20
Rate ∝
bandwidth
×
bits / symbol
×
code rate
×
spatial streams
preamble + pilots
airtime overhead
contention + ACK
MAC overhead
retries
channel loss
TCP / app
protocol overhead
Application throughput is always lower—and depends on distance, interference, clients, and scheduler behavior.
Notes: • Use this slide to inoculate students against comparing standards only by their maximum PHY rate.
• Wider bandwidth and higher QAM require suitable spectrum and SNR; more spatial streams require antennas and favorable channels; multiuser gains require traffic from multiple users.
• Ask which factor fails first when moving farther from the access point.
[Sources]
- https://www.cisco.com/c/en/us/support/docs/wireless-mobility/wireless-lan-wlan/212892-802-11ac-wireless-throughput-testing-and.html
- https://www.cisco.com/c/en/us/td/docs/wireless/controller/technotes/8-4/b_cisco_aironet_series_migrating_to802_11_ac.html

## Slide 21
WI-FI HISTORY
The MAC and security story evolves alongside the waveform
21
1997
CSMA/CA
DCF, ACK, RTS/CTS
1999
WEP
privacy goal; later broken
2004
WPA2
802.11i / CCMP
2009
aggregation
A‑MPDU / A‑MSDU
2018+
WPA3
SAE + stronger protection
2024
MLO
coordinate links
PHY innovation changes what is possible; MAC innovation determines who gets airtime and how safely.
Notes: • Keep security chronology high level: WEP's weaknesses motivated WPA as a transition and 802.11i/WPA2 as a durable redesign; WPA3 strengthens authentication and protection.
• Aggregation was essential because faster PHYs otherwise expose fixed per-frame overhead.
• MLO is both a PHY/MAC coordination story: multiple links must be discovered, negotiated, and scheduled.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://extr-p-001.sitecorecontenthub.cloud/api/public/content/3f5d887b048d49cba95392b829960d1b?download=true&v=564c5124
- https://standards.ieee.org/ieee/802.11be/7516/

## Slide 22
WI-FI HISTORY
Wi‑Fi and cellular optimize different edges of the same network
22
Wi‑Fi
unlicensed spectrum
local ownership
contention-based access
very wide local channels
rapid device ecosystem
Cellular
licensed / managed spectrum
operator control
scheduled access
wide-area mobility
integrated service guarantees
Future edge systems choose, combine, and hand off across both.
Notes: • Relate the Wi‑Fi history back to Future Edge Networks.
• Avoid a winner/loser framing: Wi‑Fi excels at locally owned, high-capacity access; cellular excels at managed wide-area mobility. Modern devices and edge services use both.
• Invite examples: campus offload, AR/VR, industrial links, fixed wireless access, and multi-access edge computing.
[Sources]
- https://standards.ieee.org/wp-content/uploads/import/documents/other/geps_07-iot_smart_cities.pdf

## Slide 23
WI-FI HISTORY
Read any new Wi‑Fi generation through five questions
23
01
What spectrum does it use?
02
What does one PPDU look like?
03
How are users separated?
04
What channel conditions does it assume?
05
Which bottleneck moved next?
b → a/g → n → ac → ax → be
Notes: • Close by asking students to apply the five questions to one generation not emphasized in class.
• Suggested check: Why can 4096-QAM increase peak rate but reduce robustness? Why can OFDMA improve efficiency without changing the total channel bandwidth? Why is 60 GHz directional?
• The durable lesson is not memorizing letters; it is recognizing the resource dimension and engineering tradeoff each amendment introduces.
[Sources]
- https://standards.ieee.org/ieee/802.11/10548/
- https://standards.ieee.org/ieee/802.11be/7516/