## Slide 1
How to Update
Your 5G vRAN
Why live software updates are hard in vRAN — and how SwapRAN approaches them
Rodney Carey
DU + CU
IN-PLACE UPDATE
CI/CD VISION
Notes: Opening: I am going to tell the story of the paper rather than walk through the rubric directly. The flow is: what changed with vRAN, why software updates become necessary, why updating vRAN is difficult, what SwapRAN changes, whether it works, and what that enables.

## Slide 2
1 • FOUNDATION
The RAN becomes software
The key shift is not just “new hardware” — it is moving RAN functions into software running on general-purpose infrastructure.
Radio Unit
(RU)
Baseband /
BBU
Core
Traditional RAN
RU
vDU
vCU
General-purpose server
+ Kubernetes / CNFs
vRAN
The consequence: RAN behavior is now software behavior — which creates a software lifecycle problem.
Source: paper §2 “5G RAN and vRAN”
Notes: Keep this brief because the class already knows RAN. The important setup is that the RAN functions are now software artifacts on general-purpose servers. That makes updates attractive in the same way updates are attractive in cloud systems.

## Slide 3
2 • MOTIVATION
Once the RAN is software, updates become part of the lifecycle
Bug fixes, security patches, performance improvements, and new features are useful only if operators can deploy them without taking service down.
Code change
Build / test
Deploy
Live RAN
Cloud software
update
Often designed around replacement, restart, or rolling deployment.
vRAN update
?
The paper’s motivating tension:
“RAN should be software-like” ≠ “RAN can be updated like a normal app.”
Source: paper intro; CI/CD motivation
Notes: This is where I implicitly answer why researchers are interested. vRAN creates an opportunity for software-style evolution, but that benefit only matters if live networks can absorb updates with little disruption.

## Slide 4
3 • PROBLEM
But vRAN has two very different update bottlenecks
DU — real-time pressure
PHY / MAC
REAL-TIME
The DU has time-sensitive processing.
Starting a second DU on the same server can compete for CPU.
Old DU
serving users
New DU
initializing
CPU contention → missed deadlines / crash risk
CU — connection/state pressure
F1
STATEFUL
SCALE
One CU can aggregate hundreds of DUs and many UEs.
Restarting it disconnects many peers at once.
DU1
DU2
DU3
DU4
DU5
all reset together
→ signaling storm / network-wide disruption
Source: paper §§2–3
Notes: The important conceptual point is that “live update” is not one problem. The DU is constrained by real-time CPU scheduling. The CU is constrained by stateful, many-to-one relationships. SwapRAN needs a different mechanism for each.

## Slide 5
4 • LANDSCAPE
Existing approaches leave a gap
STOP
↓
REPLACE
Simple deployment model
but long outage
Baseline in evaluation: ~24 s for DU / ~7 s for CU
ATLAS
Old server →
programmable switch →
new server
Faster, but extra infrastructure
Does not fit the common single-server DRAN model.
DESIRED
In-place update
+ no spare server
+ minimal disruption
+ works with the RAN architecture
This gap is where SwapRAN sits.
The paper is not trying to make updates literally zero-cost; it targets roughly normal cellular hiccup scale: about 1–2 seconds.
Source: paper §§3–4; Atlas comparison
Notes: Use this slide to position the research landscape. The paper argues that planned stop-and-replace causes tens of seconds of disruption, while Atlas-style approaches need additional infrastructure. SwapRAN instead targets an in-place update path.

## Slide 6
5 • CONTRIBUTION
SwapRAN: prepare the replacement while the old version still serves
The core design idea is to treat an update like a controlled handoff of responsibility — but using platform-level mechanisms rather than radio handovers.
OLD
RAN
NEW
RAN
SWAP
POINT
LIVE
RAN
1
Keep old version serving
2
Initialize new version
3
Transfer responsibility
4
Retire old version
DU → CPU + eSwitch
CU → F1AP proxy
No extra server
~1–2 s goal
Source: paper §§4–5
Notes: This is the contribution slide. Say the conceptual idea first, then tell the audience there are two implementations: one for the DU and one for the CU. The phrase “controlled handoff of responsibility” is a useful mental model, but SwapRAN explicitly avoids radio-layer handover as the update mechanism.

## Slide 7
6 • MECHANISM
DU update: initialize first, transfer real-time ownership second
Time →
Old DU
Serving users / RT processing
RT demotion
New DU
Non-RT init: memory, interfaces, CU handshake
RT starts
Traffic → new DU
NIC eSwitch
steers fronthaul
Key insight: most DU startup work is non-real-time initialization, so do that while the old DU is still serving.
RT-to-ready ≈ 160 ms
Blackout < 200 ms
Measured UE downtime ≈ 600 ms
Why not simply run both DUs at once? Because RT CPU competition can break the old DU.
Source: paper §5.1 and §7.1
Notes: Emphasize the separation between initialization and real-time service. SwapRAN lets the new DU do non-RT work while the old DU still serves users, then transfers RT execution. The embedded switch handles fronthaul steering because kernel-bypass networking prevents ordinary kernel routing.

## Slide 8
7 • MECHANISM
CU update: decouple the connections, then migrate DUs gradually
Without a proxy
Old CU
DU1
DU2
DU3
DU4
Restart CU → all F1 associations break at once → signaling storm
With SwapRAN
Old CU
New CU
F1AP
Proxy
DU1
DU2
DU3
DU4
Reset one DU → switch association → repeat
F1AP RESET is used to soft-reset DUs and control the migration pace.
Source: paper §5.2
Notes: The proxy is the CU contribution’s central idea. It breaks the direct dependency between the DU’s F1 connection and a particular CU process. That lets the new CU become ready before individual DUs are moved. F1AP RESET provides the standardized control operation used to migrate them one by one.

## Slide 9
8 • ARCHITECTURAL INSIGHT
Why not just use a handover?
Because “move a UE” and “replace the software hosting the RAN” are different architectural operations.
RADIO CONTROL
E2 / RIC
→ handover commands
→ radio-specific state & parameters
PLATFORM / ORCHESTRATION
O2 / SMO
→ Kubernetes API
→ CNF lifecycle / software update
No standardized
bridge at the time
of the paper
SwapRAN keeps the update at the platform layer and uses F1AP control to move DUs instead of invoking radio-level handover logic.
Source: paper §5.2 “Why not handovers?”
Notes: This is a deeper architectural point, not just an implementation detail. The paper says network-initiated handovers belong to the E2/RIC radio-control domain, while software lifecycle changes are initiated through O2/Kubernetes. At the time of the paper there was no standardized bridge between those domains, and handover itself carries many radio-specific parameters.

## Slide 10
9 • EVALUATION
The evaluation turns the architectural idea into measurable disruption
SwapRAN is evaluated on real 5G testbeds, including a commercial-grade DU setup and an open-source OAI CU setup.
DU update
~24 s
K8s baseline
~600 ms
SwapRAN
RT-to-ready ≈ 160 ms; blackout under 200 ms
CU update
~7 s
K8s baseline
~1.2 s
SwapRAN
Takeaway: update time is pushed into the “normal hiccup” range.
The goal is not zero downtime; the goal is disruption small enough that an update behaves like an ordinary cellular hiccup.
Source: paper §7 Evaluation and Results
Notes: Be precise with the DU numbers. The measured total UE downtime is about 600 ms in the evaluation, while the RT-to-ready/blackout component is under 200 ms, with RT-to-ready reduced to roughly 160 ms. The general paper target is 1–2 seconds.

## Slide 11
10 • SIGNIFICANCE
If live updates work, the next step is a software-native RAN lifecycle
SwapRAN is bigger than “a faster restart.” It makes the paper’s original CI/CD vision more plausible.
Developer
change code
CI
build + test
Orchestrator
roll out update
SwapRAN
migrate live RAN
Network
serve users
Faster iteration
→ patches and features
Operational automation
→ repeatable rollout
Safer deployment
→ monitor + rollback
This is where vRAN starts to look more like cloud infrastructure — without pretending the RAN has cloud-like timing constraints.
Source: paper introduction / CI/CD vision; implications beyond implementation
Notes: The paper explicitly frames vRAN as a path toward CI/CD-like updates. The three items at the bottom are broader implications: faster iteration, automation, and safer rollout/rollback. Present these as opportunities enabled or suggested by the work, not as features fully implemented by SwapRAN.

## Slide 12
11 • OPPORTUNITIES
The paper also exposes a broader research space
Large-scale rollout
How do we coordinate updates across thousands of sites without creating regional signaling spikes?
Failure-aware updates
What happens if the new DU/CU fails halfway through the swap? Can rollback be automatic?
End-to-end CI/CD
How do testing, policy, observability, deployment, and rollback fit around live RAN updates?
Architecture evolution
As RAN becomes more distributed and software-defined, where else can live migration replace maintenance windows?
The important shift in perspective: live updates become a systems problem spanning networking, operating systems, orchestration, and RAN control.
Notes: The paper directly demonstrates a live-update mechanism. These four are broader research directions that naturally follow from the result. Make clear which parts are your interpretation rather than claims that SwapRAN implemented all of them.

## Slide 13
12 • CONCLUSION
The story in four takeaways
1
vRAN changes the RAN from specialized hardware into software that needs an update lifecycle.
2
Live updates are difficult because the DU is real-time and the CU is stateful + highly connected.
3
SwapRAN updates both in place: CPU-aware DU startup/steering and proxy-based CU migration.
4
That pushes update disruption toward normal cellular hiccup scale and opens the door to CI/CD-style RAN operations.
Core thesis
SwapRAN shows that vRAN software can be updated with minimal disruption by treating DU/CU replacement as an infrastructure migration problem — not a radio-control problem.
Notes: Final 30–45 seconds before Q&A: vRAN creates the need, the architecture creates the difficulty, SwapRAN provides a two-part solution, and the larger implication is a path toward software-native RAN operations.