## Slide 1
NeurIPS 2023 · Collaborative Perception
How2comm
Communication-Efficient and Collaboration-Pragmatic
Multi-Agent Perception
Autonomous Vehicles
LiDAR Detection
V2X Communication
Dingkang Yang · Kun Yang · Yuzheng Wang · Jing Liu · Peng Zhai · Lihua Zhang
Fudan University
Problem 1 Communication
Redundancy
Problem 2 Transmission
Delay
Problem 3 Collaboration
Heterogeneity

## Slide 2
The Problem: Why Single-Agent Perception Isn't Enough
Single-Agent Limitations
1
Occlusions
Objects hidden behind buildings, trucks, or other vehicles are simply invisible to a single sensor.
2
Limited Range
A vehicle's LiDAR only covers a finite radius — beyond that, the world disappears.
3
Sparse Point Clouds
At distance, only a handful of points represent an object, making detection unreliable.
Multi-Agent Collaboration Helps — But Adds New Challenges
V2V / V2X communication lets vehicles share sensor data in real time — dramatically improving perception. But this introduces:
Communication Redundancy
Sharing all features indiscriminately wastes limited bandwidth.
Transmission Delay
Data arrives late, causing fast-moving objects to appear in the wrong place.
Collaboration Heterogeneity
Different LiDAR sensors create feature-space gaps that break fusion.

## Slide 3
Three Core Challenges How2comm Solves
Each challenge represents a fundamental barrier to practical collaborative perception
01
Communication Redundancy
What's happening:
Existing methods either compress everything uniformly or rely on coarse confidence maps to decide what to share.
Why it matters:
Bandwidth in real V2V/X systems is severely limited (~1 MB). Sending too much data makes real-time collaboration infeasible.
How2comm's fix:
Spatial-channel message filtering guided by mutual information — send less, but preserve the most useful semantics.
02
Transmission Delay
What's happening:
Data is always transmitted from the past (t₀ = t − τ). A car moving at 60 mph travels ~3 meters in 100ms.
Why it matters:
Feature misalignment makes collaboration actively harmful — fused data can place objects in the wrong location.
How2comm's fix:
Flow-guided future feature prediction warps past features forward in time to align with the current frame.
03
Collaboration Heterogeneity
What's happening:
Different agents (vehicles, infrastructure) have different LiDAR hardware — density, range, noise characteristics all differ.
Why it matters:
Naive feature fusion causes feature-space mismatches, and fails to exploit the distinct advantages of each agent's viewpoint.
How2comm's fix:
STCFormer decouples features into exclusive and common perception regions, handling each appropriately.

## Slide 4
How2comm: System Overview
1. Encode
Shared PointPillar encoder converts LiDAR point clouds to BEV feature maps for all agents
2. Filter
MIC module: spatial-channel attention selects only the most informative features to transmit
3. Predict
FDC module: feature flow warps collaborator features forward to current timestamp t
4. Fuse
STCFormer integrates decoupled spatial semantics + temporal context across agents
5. Detect
Regression and classification decoders output 3D bounding boxes for objects
Key design principle: Agents operate asynchronously. The ego vehicle broadcasts what it needs; collaborators send only what fills those gaps. All collaboration happens in intermediate feature space — not raw sensor data (too large) and not final predictions (too lossy).

## Slide 5
How2comm: System Overview
1. Encode
2. Filter
3. Predict
4. Fuse
5. Detect

## Slide 6
Module 1 — Mutual Information-Aware Communication (MIC)
Goal: transmit less data while preserving the most semantically valuable information
How It Works
1
Step 1 — Ego Generates Queries
The ego vehicle computes spatial attention (which locations matter?) and channel attention (which feature dimensions matter?) for its own BEV feature map.
2
Step 2 — Ego Broadcasts Requests
It inverts these attention maps (1 − A) to produce a 'request' signal: what spatial regions and channels does the ego lack?
3
Step 3 — Collaborator Responds
The collaborator combines the ego's requests with its own attention to produce a binary mask M, then sends only F̃ = F ⊙ M — a sparse, targeted feature.
4
Step 4 — Mutual Info Supervision
A Jensen-Shannon divergence loss L_mul ensures the sparse filtered features retain the most critical semantics of the full original features.
Why This Is Better
✗
Previous: Feature Compression
Autoencoders compress everything uniformly — valuable features get squashed alongside irrelevant ones.
✗
Previous: Spatial Filtering Only
Confidence maps pick locations but ignore which feature channels matter — half the picture.
✓
How2comm: Both Dimensions
Spatial AND channel filtering, guided by what the ego actually needs — targeted, not uniform.
✓
Bonus: Info Preservation
The MI supervision loss prevents important semantics from being lost in the filtering process.

## Slide 7
Module 2 — Flow-Guided Delay Compensation (FDC)
The Core Problem: At 100ms delay (typical V2X), a vehicle moving at 60 mph has traveled ~2.7 meters. Fusing features from different timestamps causes false positives, ghost objects, and missed detections — collaboration makes things worse, not better.
t₀−k
Historical frame
(collaborator)
t₀
Last transmitted
frame (delayed)
t
NOW
(ego's frame)
FDC predicts forward →
Step 1: Flow Generation
The collaborator runs its historical feature sequence {F^(t₀−k), ..., F^t₀} through a flow generator network to produce a feature flow O^t₀ (direction) and scale matrix S^t₀ (magnitude).
Step 2: Feature Warping
The ego receives the sparse feature F̃^t₀, the flow O^t₀, and scale S^t₀. It estimates the predicted future feature: Z^t = warp(F̃^t₀, (t−t₀)·O^t₀) ⊙ S^t₀
Step 3: Self-Supervised Training
No motion annotations exist in the datasets, so the flow generator is trained by maximizing cosine similarity between the predicted feature Z^t and the actual future feature F^t (used as a proxy label).

## Slide 8
Module 3 — Spatio-Temporal Collaboration Transformer (STCFormer)
Goal: pragmatic fusion that handles heterogeneous agents and learns from history
⏱ Temporal Cross-Attention (TCA)
Problem it solves
Point cloud sparsity makes it hard to detect fast-moving objects in a single frame.
How it works
Uses Q-K-V attention across the ego's current frame and all merged historical features (from both ego and collaborators). A 1D temporal convolution extracts sequential dependencies before attention.
Key benefit
Historical context fills in gaps left by sparse or occluded current observations.
🔀 Decoupled Spatial Attention (DSA)
Problem it solves
Naively fusing all collaborator features ignores the structural difference between shared and unique viewpoints.
How it works
An importance generator scores each spatial location for both ego (I^t_i) and collaborator (I^t_j). The collaborator's features are split into: Exclusive Map (1−I^t_i)⊙I^t_j — what only they see; Common Map I^t_i⊙I^t_j — what both see. Separate deformable attention heads handle each.
Key benefit
Exclusive features fill blind spots; common features bridge sensor discrepancies.
⚖ Adaptive Late Fusion (ALF)
Problem it solves
Exclusive and common features have different informational value at different spatial locations.
How it works
Two weight maps G^t_e and G^t_c are learned via 1×1 convolutions and softmax. Final output: F^t_i = G^t_e ⊙ F^t_e + G^t_c ⊙ F^t_c — an adaptive, spatially-varying blend.
Key benefit
Better than simple addition — the network learns where to trust exclusive vs. common information.

## Slide 9
The Decoupling Intuition: Why Split Features at All?
Key insight from the paper: In a typical V2X scene, a collaborator has two types of useful information for the ego agent — things they both see (common region) and things only the collaborator sees (exclusive region). These require fundamentally different handling.
EXCLUSIVE REGION
(Infrastructure sees, ego does not)
▸ This is the collaborator's biggest value-add — compensating for the ego's blind spots.
▸ Typical example: infrastructure camera sees around a corner, or over an occluding truck.
▸ Without this information, the ego would simply miss these objects.
▸ ESA uses deformable attention to sample keypoints specifically in this exclusive zone.
COMMON REGION
(Both agents see the same area)
▸ Both agents observe this area but with DIFFERENT sensors — different LiDAR hardware creates feature gaps.
▸ Common region features help the framework bridge the sensor discrepancy / heterogeneity problem.
▸ CSA fuses these complementary views to produce a more robust representation of shared space.
▸ Result: localization errors and feature mismatches are significantly reduced in shared areas.

## Slide 10
Quantitative Results: How2comm vs. State of the Art
+8.4%
AP@0.7 improvement
on DAIR-V2X (real-world)
+7.0%
AP@0.7 improvement
on OPV2V (simulated)
3 datasets
DAIR-V2X · V2XSet · OPV2V
All outperform prior SOTA
Model
DAIR-V2X
AP@0.5/0.7
V2XSet
AP@0.5/0.7
OPV2V
AP@0.5/0.7
No Fusion
50.0 / 43.6
60.6 / 40.2
68.7 / 48.7
When2com
46.6 / 32.5
65.1 / 41.9
70.6 / 53.7
V2VNet
52.2 / 38.6
79.1 / 49.3
77.5 / 62.1
DiscoNet
51.4 / 40.0
79.8 / 54.1
81.1 / 64.9
V2X-ViT
51.7 / 40.0
83.6 / 61.4
80.6 / 66.4
CoBEVT
56.1 / 41.5
81.1 / 54.3
81.6 / 67.5
Where2comm
59.3 / 43.5
82.0 / 53.4
82.8 / 67.3
How2comm ✓
62.4 / 47.2
84.1 / 67.0
85.4 / 72.2

## Slide 11
Communication Efficiency: Better Performance, Less Bandwidth
📷 Insert Figure 4 here
(Communication Volume vs. AP@0.7 across all 3 datasets)
Key Takeaways
Dominates at all bandwidth levels
How2comm outperforms Where2comm (the prior best) across every tested communication budget — not just at a specific sweet spot.
Matches SOTA with less data
At lower communication volume, How2comm achieves comparable AP to models that transmit far more — a fundamentally better efficiency curve.
Spatial-channel filtering works
The MIC module is the key driver: by sending targeted features rather than uniform compressions, each byte transmitted carries more useful information.
MI supervision prevents degradation
Without the mutual information loss, aggressive filtering would drop useful semantics. The supervision term keeps quality high even at high sparsity.

## Slide 12
Robustness: Surviving Real-World Noise
Real deployments are messy. How2comm was stress-tested under three types of noise:
Localization Error
GPS / positioning drift (0–0.5m std dev)
What it simulates
Agents don't know their exact position — a realistic problem in urban canyons and GPS-denied environments.
How2comm's performance
Stays above all baselines and above 'No Fusion' at all error levels. Some methods (V2VNet, When2com) fall below No Fusion beyond 0.2m — collaboration actively hurts them.
Heading Error
Orientation/yaw noise (0–1.0° std dev)
What it simulates
Even small rotational errors in how an agent thinks it's facing cause significant feature map misalignment when projected to ego coordinates.
How2comm's performance
Maintains the largest margin over competing methods. The STCFormer's attention mechanism is robust to small spatial misalignments by design.
Transmission Delay
Temporal lag of 0–400ms
What it simulates
Network congestion, processing overhead, and wireless channel variability all contribute to delayed data in real V2X systems.
How2comm's performance
Improves AP@0.7 by 7.5% over No Fusion even at severe 400ms delay on DAIR-V2X — the FDC module directly compensates by predicting future features.

## Slide 13
Robustness: Surviving Real-World Noise
Real deployments are messy. How2comm was stress-tested under three types of noise:
Localization Error
GPS / positioning drift (0–0.5m std dev)

## Slide 14
Robustness: Surviving Real-World Noise
Real deployments are messy. How2comm was stress-tested under three types of noise:
Heading Error
Orientation/yaw noise (0–1.0° std dev)

## Slide 15
Robustness: Surviving Real-World Noise
Real deployments are messy. How2comm was stress-tested under three types of noise:
Temporal lag of 0–400ms
Transmission Delay
Temporal lag of 0–400ms

## Slide 16
Conclusion & Future Work
How2comm is the first framework to jointly address all three core challenges of collaborative perception
MIC
Mutual Info-Aware Communication
Send less, but better — spatial-channel filtering with MI supervision preserves critical semantics under bandwidth constraints.
FDC
Flow-Guided Delay Compensation
Predict the future — feature flow warping aligns collaborator data to the current timestamp, defeating the transmission delay problem.
STCFormer
Spatio-Temporal Collaboration Transformer
Think holistically — decoupled exclusive/common spatial attention + temporal context produces robust, heterogeneity-aware fusion.
Results: SOTA on DAIR-V2X (+8.4% AP@0.7), V2XSet, and OPV2V (+7.0% AP@0.7) · Superior under localization error, heading error, and transmission delay
Limitation
Only exploits short-term historical frames for temporal context. Long sequences are left for future work.
Future Work
(1) Long-term temporal modeling with extended point cloud sequences. (2) Uncertainty-aware feature flow prediction for more reliable warping.