## Slide 1
NSDI '26 · Yibin Shen & Zili Meng, HKUST
Law: bounding latency on the Wi-Fi last hop
Why this paper: the queues, retries and rate adaptation are exactly what cause latency spikes, and Law redesigns the link layer to bound them.
Paper: “Law: Towards Consistent Low Latency in 802.11 Home Networks” · Talk: youtube.com/watch?v=BAT-DEx037c
Notes: My paper was Law which is by Yibin Shen and Zili Meng at HongKong university of science and tech.
Lookint at the history of wifi we can see how Wi-Fi grew queues, retransmissions and rate adaptation and how each of those are added for throughput, reliability or fairness.
This paper shows that those same three mechanisms are what make latency spike on a home Wi-Fi link, and it redesigns them so that no packet will sits for longer than a fixed amount of time.
The trick that makes this possible is something only a real-time video application can offer, which is tolerance for losing a few packets.

## Slide 2
WHY THIS PAPER
Two reasons it belongs in this course
01
It closes the loop on the history of Wi-Fi
Queues, retries and rate adaptation were each added to Wi-Fi for throughput, reliability or fairness. Together, they are exactly what makes latency spike.
02
It uses something only video can offer
Real-time video already survives a little loss. Law lets the link layer spend that tolerance to put a hard cap on delay.
Law · NSDI '26 — 02
Notes: There are two reasons we picked this paper.
Layered queues, retries and rate adaptation were each added to Wi-Fi to make it faster, more reliable or fairer. This paper shows that, working together, those same mechanisms are what cause latency spikes.
Second, it takes advantage of something video apps can do: live video can handle losing a few packets. It has tools to cover for them, like forward error correction, or FEC, which sends a bit of extra data to rebuild lost packets. So Law makes a trade: and it gives up a little loss in exchange for a hard cap on delay.

## Slide 3
THE PROBLEM
The average is fine, but the tail is not
100 ms
End-to-end deadline for cloud gaming, met 99.9% of the time or better
25 ms
Median latency for mobile devices today, thanks to CDNs and edge servers
>200 ms
99.9th-percentile frame delivery latency measured over Wi-Fi (Augur)
Ultra-low-latency apps (cloud gaming, video calls, mixed reality) are judged by their worst frames, not their typical one.
Law · NSDI '26 — 03 · Sources: paper 1–2.1, Table 1
Notes: Ultra-low-latency applications impose really really strict latency requirements. Think gaming right? A fighting game or a shooter game rely on incredible precision and accuracy and timing from a gameplay standpoint.
so usually cloud gaming wants under 100 ms end to end, as reliably as 99.9% of the time if not better. On average it is already good around 25 ms. But the tail is the problem – the tail referring to the slowest packets of the bunch.
previous measurements found that 99.9th-percentile frame delivery latency was above 200 ms. So there's a big gap between typical and consistent low latency, and consistency is what these apps and games really need. YoU dont need usually fast, you need "always" fast

## Slide 4
WHERE THE TAIL COMES FROM
The Wi-Fi last hop now dominates the tail
The backbone has been optimized. Edge servers sit within about 10 ms one way, and base RTT is under 20 ms in 90% of cloud-gaming sessions. What's left is the last hop.
Wi-Fi's share of end-to-end latency, when end-to-end latency exceeds 70 ms
>95%
Queueing delay's share of last-hop latency, when the last hop exceeds 70 ms
>80% on average
Law · NSDI '26 — 04 · Two-week campus measurement, paper Fig. 3–4
Notes: So why focus on Wi-Fi? Because the rest of the path has been getting really really fast
Services like Netflix, YouTube and cloud gaming use CDNs, content delivery networks. These are servers spread around the world that keep copies of content close to you. Thanks to CDNs and nearby edge servers, you can usually reach a server in about 10 milliseconds one way. One study found the round trip took under 20 milliseconds in 90% of cloud-gaming sessions.
you can probably reach a nearby server within about 10 ms one way, and one recent study found base roundtrip time under 20 ms in 90% of cases.
The authors measured this on their campus for two weeks. Whenever total delay went over 70 milliseconds, more than 95% of it came from the Wi-Fi last hop the wireless jump from the router to your device. And when they broke that down, more than 80% of the Wi-Fi delay was packets waiting in line, or queueing.
So the tail is really a waiting-in-line problem, right at the last hop.

## Slide 5
BACK TO THE HISTORY
Three familiar mechanisms, built for other goals
Mechanism | What it was built for | What it does when the channel dips
Layered queues MAC flow queues → driver retry queues → hardware FIFO (up to 8) | Throughput and fairness, like multi-level caching | Each layer has its own scheduler and adds its own delay; no layer sees the total
Retries Hardware retries, then software retries; ath9k gives up after 31 | Reliability: keep loss near zero | One stubborn packet can cost up to hundreds of ms and blocks every packet behind it
Rate adaptation Minstrel and similar, picking the MCS | Goodput, judged from channel quality alone | Slows the sender when the channel fades, so the queue grows even faster
Law · NSDI '26 — 05 · Paper 2.2
Notes: The paper's core argument is that Wi-Fi was never designed for super-low-latency apps. Like I said before, it was designed for speed, reliability and fairness.
So That leaves three gaps.
One: there are too many waiting lines. A packet waits in the operating system's Wi-Fi queue, then in the driver's queue for retries, then in the Wi-Fi chip's own queue of up to 8 frames. Each line is managed separately, and none of them knows about the others.
Two: retries ignore time. When a send fails, the chip waits a moment and tries again, and again. Failed packets even get sent back for more rounds. One widely used driver only gives up after 31 attempts, and that can take over 100 milliseconds, while every packet behind it waits.
Three: rate adaptation ignores the queue. It picks a speed based only on signal quality. So when the signal gets shaky, it slows down, even while packets keep piling up in line.

## Slide 6
ANATOMY OF A SPIKE
How the three mechanisms compound ( in one real trace )
1
Channel dips
Packet 11 is lost: the channel has started to fluctuate.
2
Retries pile up
~15 ms to send one frame, ~25 ms for one aggregate. Everything behind waits.
3
Rate drops
Around packet 21, rate adaptation lowers the MCS: sending slower while the queue still fills.
4
Queue drains slowly
Queueing delay climbs to ~80 ms and falls back only gradually.
Delay rises fast and falls slowly, because no single layer can shed what the others have queued.
Law · NSDI '26 — 06 · 60-packet real-world trace, paper Fig. 7
Notes: Here's a real trace of 60 packets from the paper.
At packet 11, a packet is lost. The signal has started to get shaky. The packets after it go through tons of retries: about 15 milliseconds just to get one frame through, and about 25 for a bundle of frames. So the line starts building and piling up
Around packet 21, rate adaptation lowers the speed setting. It wants to send slower when the signal is not steady or consistent. But now we're sending slower and the line is still getting bigger and bigger, so the waiting time climbs even more, up to about 80 milliseconds.
And in that case the delay shoots up fast but comes down slowly. With multiple layers of queues, no single layer can clear what the others have piled up.

## Slide 7
WHY NOT JUST TUNE IT?
The obvious fixes make things worse
Cap each layer
25 ms limit on MAC flow queues; hardware queues capped at 8 frames.
8.0× the loss, and 99.99th-pct latency still ~200 ms
Remove the hardware queue
Each send now waits on an interrupt to fetch the next frame, and the idle channel is lost to other devices.
2.5× the loss, and 99.99th-pct latency over 400 ms
Retry less
The share of packets needing retries varies up to 15× across common signal strengths.
A fixed retry cap is too loose at one RSSI and too harsh at another
The structure is the problem, not any one parameter.
Law · NSDI '26 — 07 · Paper 2.2, 3.1, Fig. 8 and 11
Notes: Before proposing Law, the authors show that the obvious fixes or tweaks don't work.
First fix: put a time limit on each line. A 25-millisecond limit on the first queue, and the chip's queue capped at 8 frames. Result: packet loss goes up 8 times, and the slowest 1 in 10,000 packets still take almost 200 milliseconds.
Second fix: just remove the chip's queue. Now, before every send, the chip has to stop and ask the driver for the next packet. On shared Wi-Fi, someone else grabs that moment of stopping, so you would just keep missing your chance to send. The slowest packets now take over 400 milliseconds, and loss goes up two and a half times.
Third fix: just retry less. That doesn't work either. How many retries a packet needs changes by up to 15 times depending on signal strength. So any fixed limit is too loose in some places and too harsh in others.
In short: tweaking settings isn't enough. You have to redesign the structure.

## Slide 8
THE KEY INSIGHT
Dropped beats blocked
For real-time video, a packet that arrives too late is as useless as one that never arrives, and the app already knows how to cover for a lost one.
Notes: This is the key takeaway and the reason the paper is relevant. For ultra-low-latency applications, getting dropped at the could potentially be more beneficial than getting blocked. A late frame is useless, but a lost packet can be recovered. So instead of queueing and retrying a packet for a long time, drop it early and let the upper layers recover.

## Slide 9
WHAT VIDEO OFFERS THE LINK LAYER
Three layers above already absorb small losses
Forward error correction
WebRTC FEC at 1/8 redundancy absorbs 1% extra loss, adding at most one RTT to 99.9th-pct frame latency.
Error concealment
Codecs such as H.264 reconstruct lost data and frame skipping and neural codecs push loss resilience further.
Delay-based congestion control
GCC tolerates 2% loss without cutting its rate and BBR tolerates at least 5% random loss.
The catch: FEC repairs only so many losses per frame or group, so the pattern of loss matters as much as the rate.
Law · NSDI '26 — 09 · Paper 2.3, Fig. 10
Notes: So that loss tolerance comes from Three different places.
First, forward error correction. The authors tested it with WebRTC, the technology behind most browser video calls. They added 1% extra packet loss, and the slowest frames got slower by at most one round trip. Barely noticeable.
Second, error concealment. Video formats like H.264 can patch over missing data so the picture still looks right. And even newer formats can push that even further.
Third is, congestion control that watches delay instead of loss. GCC, which WebRTC uses, doesn't slow down for up to 2% loss, and BBR handles at least 5%.
But here's the catch, and it shapes Law's whole design. FEC can only fix a few losses at a time. Lose too many packets in a row, and it can't rebuild them. So the link layer has to control not just how many packets it drops, but how bunched together those drops are. Spread out is fine; bursts are not.

## Slide 10
LAW, PART 1 · QUEUE RESHAPING
One queue, one latency bound
TODAY (ath9k / OpenWiFi)
MAC · flow queues per traffic class
Driver · retry queues for software retries
Hardware · TX FIFO, up to 8 frames
Three schedulers, three separate delays
LAW
MAC · bypassed
Driver · the one queue; drop any packet waiting over Limit_q
Hardware · at most 2 frames, one sending and one ready; each stops after Limit_h
A failed frame gets one software retry, straight back to hardware
Every packet's link-layer delay
≤ Limit_q + 2 × Limit_h = 40 + 2×3 = 46 ms
Law · NSDI '26 — 10 · Paper 3.3, Fig. 12 · 40 ms / 3 ms are the evaluation defaults
Notes: So this is the design.
the design itself. Part one reshapes the queues.
Law merges the waiting lines into one. It moves the first queue down into the driver and removes the driver's retry queue. The chip keeps at most two frames: one being sent, and one ready to go.
They keep 2 frames because if a frame finishes and nothing is ready, you miss your chance to send. That's exactly what went wrong in the second fix we just saw. And if a frame fails, it gets one retry, sent straight back to the chip at a newly chosen speed.
With one queue, delay is managed in one place. Any packet that waits in the driver longer than 40 milliseconds gets dropped. And each frame gets at most 3 milliseconds on the chip before it's pulled back.
So every packet's delay is capped at 40, plus 3 for the frame being sent and 3 for the one waiting. That's 46 milliseconds with the settings they tested.

## Slide 11
WHY ONE BOUND BEATS THREE
Per-layer budgets drop packets that would have made it
Three budgets of 10 ms each
Flow queue
12 ms > 10
Driver
4 ms
Hardware
4 ms
Dropped, at 20 ms total
One budget of 30 ms
12 + 4 + 4 = 20 ms of 30
Delays in separate layers rarely peak together, so their sum bunches near the median and fewer packets cross a single bound.
Delivered
Law · NSDI '26 — 11 · Paper Fig. 13–14
Notes: So why merge the queues? Why not just put a time limit on each one?
If we were to need, say want 30 milliseconds total, and we split it evenly: 10 per layer. Now picture a packet that waits 12 milliseconds in the first queue, then 4 in each of the others. Its total is 20, well under 30. But it blew past the first layer's 10-millisecond limit, so it gets dropped. The same thing can happen at the driver or the chip.
Those are pointless losses. With one queue and one 30-millisecond limit, that packet makes it through.
There's also a statistical reason. The layers rarely all get slow at the same moment. So when you add their delays together, the total tends to stay close to average, and fewer packets cross one big limit than cross three small ones.
One queue, one limit, fewer unnecessary drops.

## Slide 12
LAW, PART 2 · RATE AND RETRY CONTROL
Rate and retries, decided for every transmission
Inside Cleanup
No software retries, at most 2 hardware tries, and two drops in a row lower the rate one step.
Loss-pattern guard
After three losses in a row, the next packet gets one extra retry, keeping losses spread out for FEC.
Len_max = Limit_q·S_n / T_n
Packets the link can clear within the bound, from running averages of success rate and airtime.
Law · NSDI '26 — 12 · Paper 3.4, Fig. 15, Algorithm 1
Notes: Part two decides the sending speed and the number of retries together. There are two big changes.
First is timing. Normal rate adaptation picks a speed once in a while. Law re-decides every single time it gets a chance to send, even for a packet that's already on the chip.
Second is a Cleanup mode. Look at the three states. Stable is normal operation. After a long enough streak of successful sends, Law moves to Probing: it tries the next faster speed on two packets and keeps it only if nothing was lost and it really was faster. Otherwise it goes back.
Law can switch to Cleanup in two cases: if a packet has waited more than 40 milliseconds, and gets dropped; or the line is longer than the link can clear in time. In Cleanup, Law sends fast and retries less, no retries from the driver, at most two tries on the chip.
if two packets drop in a row, it steps the speed down one notch.
That clears the line quickly, but it could cause losses in a row, which can’t be fixed. So there's a safety guardrail: after three losses in a row, the next packet gets one extra retry.
The goal is simply get as much useful data through as possible, with a delay capped and losses kept to what the app can recover from.

## Slide 13
RESULTS · PACKET LEVEL
The tail gets cut off, (@<1% loss)
OpenWiFi on a software-defined radio (802.11n, 20 MHz, one antenna) · 10 Mbps UDP · runs of 10+ minutes · vs Minstrel, LLRA and Thompson sampling
75–83%
lower 99.9th-percentile per-packet latency
<1%
average loss, with the lowest loss-plus-deadline-miss total
16–56%
fewer bursts of five consecutive losses
Law's latency distribution graph stops sharply near 60 ms (the link bound plus the wired hop and kernel); every baseline keeps a long tail.
Law · NSDI '26 — 13 · Paper 4.2, Fig. 16
Notes: Does it actually work? They built Law on something called OpenWiFi, an open-source Wi-Fi system on a programmable radio board. They needed it because Law has to control the chip's retries directly, which normal Wi-Fi chips don't allow.
For the first test, they used a tool called iPerf to send a steady 10 megabits per second of UDP traffic through the Wi-Fi, for at least 10 minutes per run. They compared Law against three existing rate-adaptation methods: Minstrel, which is Linux's default; LLRA, which is latency-aware; and one based on Thompson sampling, a machine-learning technique.
Results: for the slowest 1 in 1,000 packets, Law cuts delay by 75 to 83 percent. And the delay stops sharply around 60 milliseconds: that's the 46-millisecond cap plus the wired part of the path. The other methods have a long tail.
Average loss stays under 1%. And even though Law drops more packets on purpose, it has 16 to 56 percent fewer bursts of five losses in a row. So the safety guard is working.

## Slide 14
RESULTS · WEBRTC VIDEO
Real video: fewer late frames, no bitrate penalty
WebRTC sender on an edge server · 10 Mbps target · 30 fps
Metric | Law vs. baselines
99th-percentile frame delivery latency | 50.6–70.3% lower
99.9th-percentile frame delivery latency | at least 58.4% lower
Frames missing the 100 ms deadline | 69.8–78.5% fewer
Average video bitrate | slightly higher
99.9th pct vs. commercial routers (MIMO or 802.11ac) | 18.6–46.0% lower
Law · NSDI '26 — 14 · Paper 4.3, Fig. 17 and 19
Notes: Now the real test was actual video. They streamed WebRTC video from a nearby edge server, at 10 megabits per second and 30 frames per second.
For the slowest 1 in 100 frames, Law cuts delay by 50 to 70 percent. For the slowest 1 in 1,000, by at least 58 percent. And frames that miss the 100-millisecond deadline drop by 70 to 78 percent.
The video quality even went up slightly compared to all three baselines. So the video app isn't slowing itself down because of Law's drops.
They also tested against real commercial routers with better hardware: more antennas and newer Wi-Fi. They matched them on signal strength or speed to keep it fair. Typical delay was about the same, but for the slowest 1 in 1,000 frames, Law was still 19 to 46 percent faster.

## Slide 15
THE TRADE, MADE VISIBLE
Law loses more often, but more lightly
≈2×
as many frames lose at least one packet
−65%
frames that lose more than 20% of their packets
In one three-frame trace, Law dropped 6 packets (≈10%), five of them in Cleanup. FEC recovered them and every frame met the 100 ms deadline.
Law · NSDI '26 — 15 · Compared with Thompson sampling, paper Fig. 18
Notes: This slide sums up the idea in two numbers, which I think is really cool. Compared with the Thompson-sampling method, Law nearly doubles the number of frames that lose at least one packet. But it cuts the frames that lose more than 20% of their packets by 65%.
That's exactly the trade-off we want, lots and lots of small losses that FEC can fix, instead of a few big ones it can't.
One example from the paper makes it concrete. Across three frames, Law dropped six packets, nearly 10%. Five of those drops happened in Cleanup. FEC recovered every one. And because Law kept the speed high, all three frames arrived within 100 milliseconds.

## Slide 16
LIMITS AND OPEN QUESTIONS
What Law assumes, and what it leaves open
Not every flow tolerates loss
Loss-based TCP (Reno, Cubic) would suffer. Law needs to tell flows apart via DSCP, whitelists or traffic patterns left as future work.
A research prototype
Built on OpenWiFi (802.11n, 20 MHz, one antenna). Shipping it needs vendors to expose per-frame hardware retry control.
Plays well with others
BBR throughput stays comparable, fairness holds for BBR and GCC, and AQM such as CoDel could still run on the driver queue.
Law · NSDI '26 — 16 · Paper 4.4, 5, Appendix A
Notes: A few caveats, so
First, the whole design depends on loss tolerance, right? But some traffic doesn't tolerate loss. Regular TCP, like Reno or Cubic, which a lot of downloads use, treats every lost packet as a sign to slow way down. So Law's drops would hurt it. A real router would need to tell the two kinds of traffic apart and only use Law for things like video. One idea: latency-sensitive traffic keeps the line short, while regular TCP tends to fill it up. So you could spot them by how they behave. The authors leave that as future work.
Second, it's a prototype. It runs on a research radio with literally one antenna and older Wi-Fi. And it needs direct control over the chip's retries, which commercial Wi-Fi chips would have to open up.
On the bright side, regular downloads using BBR, Google's congestion control, run just as fast through Law as through the other methods. Law still shares the link fairly between users. And it works alongside existing queue-management tools rather than replacing them.

## Slide 17
TAKEAWAYS
Key Takeaways
01
The Wi-Fi last hop now dominates tail latency for real-time apps.
02
Its queues, retries and rate adaptation were built for throughput and reliability, not deadlines.
03
Video tolerates a little loss, so the link layer can drop early instead of queueing long.
04
Law bounds link-layer delay with one queue and per-transmission control, at under 1% well-spread loss.
For discussion -> should we trade the reliability it was built for, in exchange for a deadline?
Notes: So, wrapping uphere there are four takeaways which actually match thee authors' own.
One: the Wi-Fi last hop is now the main cause of the worst delays for real-time apps. A chain is only as strong as its weakest link, and right now that link is Wi-Fi.
Two: Wi-Fi's queues, retries and rate adaptation were designed for speed, fairness and reliability, not for consistently low delay.
Three: because video apps can handle a little loss, there's a new design option: drop packets early instead of letting them wait too long.
Four: Law does exactly that. It caps delay, keeps losses small and spread out, and still keeps data flowing fast. In other words, it gives up a little reliability to meet deadlines.
system give up a bit of reliability to hit a deadline?

## Slide 18
RICARDO FURST – CIS5930
Thank you!